## Slide 1
LSON3.9F LSON4F LSON4.8F LSON6F LSON8F LSON10F
FEATURES
MODULE DESIGN
Iron or aluminum cabinets are available
High temperature resistance <60℃ Max
IP65 for front side and IP54 for rear side
Front service
High contrast ratio > 4000:1
LSON series LED panels are designed for outdoor regular applications
LSONF SERIES LED PANEL
www.leyard-linso.com
PRODUCT IMAGE
DESIGNED FOR OUTDOOR APPLICATIONS

## Slide 2
Linso Culture & Technology (Shanghai) Co., Ltd
ADD:NO1259,Jiamei Road,Nanxiang Town,Jiading District,Shanghai,201802,China.
Tel:+86-21-69927037 Fax: +86-21-69927035
Email:sale@linso.com.cn
Website:www.leyard-linso.com
TECHNICAL PARAMETERS
Remark: Above data is subject to change without previous notice
Item | LSON3.9F | LSON4F | LON4.8F | LSON6F | LSON8F | LSON10F
Pixel | 3.9mm | 4mm | 4.8mm | 6.67mm | 8mm | 10mm
Pixel Idensity/m² | 65536 | 62500 | 43264 | 22500 | 15625 | 10000
Module size(mm) | 250*250 | 320*320 | 250*250 | 320*320 |  | 
Cabinet size(mm) | 1000*1000 | 960*960 | 1000*1000 | 960*960 | 960*960 | 960*960
Material | Iron cabinet |  |  |  |  | 
Weight （KG/sqm） | 40 |  |  |  |  | 
Gray level | 65536 |  |  |  |  | 
Color process(Bit) | 14~16 bits |  |  |  |  | 
Refresh rate（Hz） | >3840 Hz |  |  |  |  | 
Drive mode/scan | 1/8 scan | 1/10 scan | 1/6 scan | 1/6 scan | 1/5 scan | 1/2 scan
Brightness（cd/m2） | 5000~5500 | 5000~5500 | 5000~5500 | 5500~6000 | 5500~6000 | 
Viewing angle H（°） | 140/120 |  |  |  |  | 
Input Voltage（V） | AC110~240V |  |  |  |  | 
Input frequency（Hz） | 50/60Hz |  |  |  |  | 
Power consumption M （W/m²） | 960W | 850W | 850W | 800W | 800W | 800W
Power consumption A （W/m²） | 320W | 280W | 280W | 260W | 260W | 260W
Common cathode design options | NO | NO | NO | YES(550W max) | YES(550W max) | YES(550W max)
Working Temperature（ ℃） | -10~60 |  |  |  |  | 
Working humidity(%) | 30%~85% |  |  |  |  | 
IP level(F/R) | IP65/IP54 |  |  |  |  | 
Service method | Front | Front | Front | Front | Front | Front