## Slide 1
LSX1.28 LSX1.56 LSX1.66 LSX1.86 LSX2 LSX2.5 LSX3
FEATURES
STRUCTURE
Black LED, high contrast ratio,High refresh rate, no ghosting
Silicone frame and customized PCB with bigger bended angle
Embedded 18 pcs strong magnets with better flatness
Perfect alignment no gaps & great flatness
Bigger viewing angle 160°/ 160°
Anti fire / corrosion material
Diameter ≥500mm
LSX series LED panels are more flexible and suitable for cylinder, convex & concave applications
LSX SERIES LED PANEL
www.leyard-linso.com
APPLICATION
DESIGNED FOR CYLINDER,CONVEX & CONCAVE APPLICATIONS
85mm
≥φ500mm

## Slide 2
MODULE & CABINET DESIGN
Module size is 320x160mm with 18 pcs strong magnets,support front/back service
Convex design
Concave and convex design

## Slide 3
TECHNICAL PARAMETERS
Model Name |  | LSX1.28 | LSX1.56 | LSX1.66 | LSX1.86 | LSX2 | LX2.5 | LSX3
Technical parameter | Pixel configuration | RGB 3 in 1 |  |  |  |  |  | 
 | LED encapsulation | SMD1010 | SMD1212 | SMD1212 | SMD1515 | SMD1515 | SMD1515 | SMD1515
 | Pixel density（dots/m2） | 610351 | 406406 | 360000 | 288906 | 250000 | 160000 | 105625
 | Module size（mm） | 320x160x8.6mm |  |  |  |  |  | 
 | Module resolution | 250x125 | 204x102 | 192x96 | 172x86 | 160x80 | 128x64 | 104x52
 | Scan method | 1/63 | 1/51 | 1/48 | 1/43 | 1/40 | 1/32 | 1/26
 | Refresh rate（Hz） | ≥3000-3840 |  |  |  |  |  | 
 | Frame Frequency（Hz） | 50&60 |  |  |  |  |  | 
 | Gray scale（bit） | 12-16 adjustable |  |  |  |  |  | 
 | Module shell material | Silicone |  |  |  |  |  | 
 | Module weight（kg/pcs） | 0.334 | 0.325 | 0.318 | 0.315 | 0.315 | 0.269 | 0.252
 | Cabinet size | Customized according to module size |  |  |  |  |  | 
 | Cabinet materail | Iron |  |  |  |  |  | 
 | Cabinet flatness（mm） | ≤ 0.3 |  |  |  |  |  | 
 | IP rating | IP40/IP30 |  |  |  |  |  | 
 | Installation method | Front/rear |  |  |  |  |  | 
Optical parameter | Brightness（nits） | ≥650cd |  |  |  |  |  | 
 | Color temperature（K） | 3000—10000 adjustable |  |  |  |  |  | 
 | Brightness uniformity | ≥97% |  |  |  |  |  | 
 | Viewing angle | ≥160°/≥140° |  |  |  |  |  | 
 | Contrast ratio | 5000:1 |  |  |  |  |  | 
Electric parameter | Module voltage DC（V） | 5 | 5 | 5 | 5 | 5 | 5 | 5
 | Module current DC（A） | 5 | 5 | 5 | 4.5 | 4.5 | 4.5 | 4.5
 | Module power consumotion max（w/pcs） | 25 | 25 | 25 | 22.5 | 22.5 | 22.5 | 22.5
 | Working voltage AC（V） | 110-220 |  |  |  |  |  | 
 | Max power consumption（w/m2） | 600 | 600 | 600 | 600 | 600 | 600 | 600
 | Ave power consumption（w/m2） | 200 | 200 | 200 | 200 | 200 | 200 | 200
Operation parameter | Life（hrs） | 100,000 |  |  |  |  |  | 
 | Working temperature（℃） | -10—50 |  |  |  |  |  | 
 | Storage tem（℃） | -20—60 |  |  |  |  |  | 
 | Working humidity（RH） | 20—85% |  |  |  |  |  | 
 | Storage humidity（RH） | 20—80% |  |  |  |  |  | 
Linso Culture & Technology (Shanghai) Co., Ltd
ADD:NO955,Jiamei Road,Nanxiang Town,Jiading District,Shanghai,201802,China.
Tel:+86-21-69927037 Fax: +86-21-69927035
Email:sale@linso.com.cn
Website:www.leyard-linso.com
Remark: Above data is subject to change without previous notice